## Arp spoofing

ARP (Address Resolution Protocol) spoofing is a type of cyberattack where an attacker sends falsified ARP messages over a local network. This attack allows the attacker to link their MAC address with the IP address of another device (such as the gateway), leading to:
- Man-in-the-Middle (MITM) Attacks: The attacker intercepts traffic between two devices.
- Denial of Service (DoS): Traffic gets redirected, causing network disruptions.
- Session Hijacking: The attacker can capture sensitive information.

## Set Up the Network Topology
1. Open Cisco Packet Tracer.
2. Add the following devices:
  1. 1 Router (Router0)
  2. 1 Switch (Switch0)
  3. 2 PCs (PC1 as the victim and PC2 as the attacker)
3. Connect the devices using Copper Straight-Through cables:
  1. PC1 to Switch
  2. PC2 to Switch
  3. Router to Switch
## Configure IP Addresses
1. Router Configuration (Router0)
  1. Click on the router → Go to CLI → Enter the following commands:
enable
configure terminal
interface FastEthernet0/0
ip address 192.168.1.1 255.255.255.0
no shutdown
exit
This assigns the router an IP address of 192.168.1.1.
1. PC1 (Victim) Configuration
  1. Click on PC1 → Go to Desktop → Click on IP Configuration.
  2. Set IP Address: 192.168.1.2
  3. Set Subnet Mask: 255.255.255.0
  4. Set Default Gateway: 192.168.1.1
2. PC2 (Attacker) Configuration
  1. Click on PC2 → Go to Desktop → Click on IP Configuration.
  2. Set IP Address: 192.168.1.3
  3. Set Subnet Mask: 255.255.255.0
  4. Set Default Gateway: 192.168.1.1
## Verify ARP Table Before the Attack
1. Open Command Prompt on PC1.
2. Type the following command:
arp -a
- This displays the current ARP table.
- PC1 should associate 192.168.1.1 with the router’s MAC address.
## Perform ARP Spoofing from PC2 (Attacker)
1. Open Command Prompt on PC2.
2. Run the following command to manually add a false ARP entry:
arp -s 192.168.1.1 00-11-22-33-44-55
- Replace 00-11-22-33-44-55 with PC2’s MAC address (Check in Packet Tracer by clicking on PC2 → Config → FastEthernet0).
- This tells PC1 that the attacker’s MAC address belongs to 192.168.1.1.
However  static ARP is not allowed in cisco packet tracer.

## ARP Spoofing
- Enable Dynamic ARP Inspection (DAI) on the switch.
- Use Static ARP Entries on critical devices.
- Configure Port Security to limit MAC addresses per port.
- Use ARP Spoofing Detection tools.